## Slide 1: Objects in GridDyn
GridDyn Documents
Philip Top

## Slide 2: Outline
Brief look at how the solver interacts with Griddyn
  Solve Process
  Callback functions
Objects in Griddyn
  Interface in GridCoreObjects
  Inteface in GridPrimary
  GridSecondary and GridSubModel
Specific Objects
  gridBus
  gridLink
  gridRelay
  gridArea
  gridLoad
  gridDynGenerator

## Slide 3: Execution Flow: powerflow
makeReady()
Power Balance Loop
Flow adjustment Loop
Solve*
Guess
Check/adjust*
Do Final stuff
Measure
Adjust Gen Levels
* Now we Get a little deeper

## Slide 4: Execution Flow: dynamic calculation
Calculation Initial conditions
While time<timeStop
While time<next Event Time
Find next event time
Check for roots
Deal with any issues: reset if necessary*
Save state to objects
Deal with events: reset if necessary*
finalize
Solve
* Will get into more detail in later weeks
* Now we Get a little deeper

## Slide 5: The solve Call
Call into the solverInterface solve function
  Does some flag translation and calls a solver library
Ida and Kinsol are the main solver libraries,
  Also interfaces to CVODE and ARKODE
  Simple Gauss-Seidel solver as alternative
  possibly boost::odeint later for an alternative so Griddyn can function without Sundials (not that I think it will function well, just want it to function)
SolverInterface objects have callback helper functions that call into the Griddyn simulation

## Slide 6: The solve Call (for powerflow)
GridDynSimulation
Powerflow
SolverInteface
Sundials
KLU
solve
Kinsol
ResidualFunction
Jacobian
JacobianElement*
Residual*
Function
Evaluation
Jacobian
Evaluation
* Object function calls

## Slide 7: The solve Call (for DAE)
GridDynSimulation
dyanmicDAE
SolverInterface
Sundials
KLU
solve
IDA
ResidualFunction
JacobianFunction
JacobianElements*
Residual*
Function
Evaluation
Jacobian
Evaluation
Root
Evaluation
rootFindingFunction
rootTest*
* Object function calls

## Slide 8: gridCoreObject Interface
Model Parameter Interface
set, get, setTime, setOwner
setFlag, getFlag
Object interaction
add/remove, addsp
find, getSubObject, findSubObject
Messaging/ updates
updateA, updateB
log, alert, enable, disable
getParameterString, getString
clone
Bold is not fully implemented in all objects
Notes: Addsp is for smart pointers to objects—targetted primarily at objects which are operating in multiple contexts, not used very often yet

## Slide 9: Code: GridObject

## Slide 10: Grid Object Interface
State size and indexing
setOffset, setOffsets, setRootOffset, setParamOffset,setDiffOffset, setAlgOffset,
Solution information
getState, setState, guess
Object management
IsArmed*, isConnected,
Statesize*,algsize*,diffsize*, voltageStateCount*, angleStateCount*, jacSize*, rootSize*, paramSize*,
isLoaded*, loadSize, loadSizesSub*
setupPFlowFlags*, setupDynFlags*, updateFlags
getVariableType, getTols, getConstraints
getStateNames
*Not virtual

## Slide 11: Grid Primary Interface
Initialization
pFlowInitializeA*, pFlowInitializeB*
Model calculations
preEx, jacobianElements, residual, derivative, algebraicUpdate, postEx, reset, timestep
Output
getOutput, getOutputs, getOutputLoc, getDoutDt,
getBus, getLink, getArea, getRelay
rootTest, rootTrigger, rootCheck,
pFlowObjectInitializeA, pFlowObjectInitializeB
dynInitializeA*, dynInitializeB*
dynObjectInitializeA, dynObjectInitializeB
powerFlowAdjust, pFlowCheck, reset, computePower
*Not virtual

## Slide 12: GridPrimary Notes
GridPrimary are top level simulation objects
  Areas
    Wide area controls
    Object Containers
    Simulation distribution
    Root Simulation object is special type of object
  Buses
    System nodes
    Container for loads and generators
    Compute voltage and angle
  Links
    Connect nodes together (or areas)
    Primary model of a transmission line
    But many other possibilities
  Relays
    Sensors and actuators for the grid
    Can sense from one object and act on another
Can act as containers for other primary objects and other objects

## Slide 13: GridSecondary, and GridSubModel
Very similar to gridPrimary in interface
GridSecondary
  Additional Outputs related to real and reactive power
  Additional Outputs related to available adjustments in power levels
GridSubModel
  Only one set of Initialization functions-object holding it is expected to manage when it gets initialized
  getInputSize, getOutputSize
Both
  outputPartialDerivatives –useful if the output is not a specific state
  ioPartialDerivatives --useful if the output is not a specific state
  findIndex

## Slide 14: Closer look at a function Call
virtual void residual(
  const IOdata & args,
  const stateData *sD,
  double resid[],
  const solverMode & sMode);
Input arguments (not present for gridPrimary IO data is a resizable vector class (std::vector or boost small vector)
Current state information (state, derivatives if applicable, time, id, and some other information
Storage location of calculation results
Requested method of computation and index of where to find the index information
any approximations
types of states
dynamic mode

## Slide 15: The Calculation Functions
x is the state, x’ is the derivative, t is time, y is output, z is input
Residual computes
  Some function of z, x and x’ that goes to zero when the state is self consistent
Derivative computes as a function of z and x
  For differential states only
jacobianFunction computes matrix of as function of z, x and x’
AlgebraicUpdate computes
  For algebraic states only

## Slide 16: Calculation Functions
For individual models
outputPartialDerivatives computes matrix of where y is the output and x is the internal states
  In many cases this simply 1 because the output is a state variable
ioPartialDerivatives computes matrix of for an individual object
Timestep does time advancement for an individual object independently of other objects, based on internally stored state and inputs

## Slide 17: Bus object
Voltage and angle states
  Different modes to fix one or more of the states (PQ, PV, Slack, and afix)
gridBus
gridLoads
Load 1
Load 2
Load N
.
.
.
gridDynGenerators
Gen 1
Gen 2
Gen N
.
.
.
gridLinks
Link 1
Link 2
Link N
.
.
.

## Slide 18: Bus Object
Generalized from typical power flow calculations
  The individual objects do the calculations of real and reactive power
  Busses just do the sums
  This allows expansion of loads, gens and links beyond the typical power system models in power flow and dynamic computations
For dynamic computations busses also calculate bus frequency as a filtered and scaled derivative of the angle
The only assumptions buses make about the nature of generators, loads and links is that they are functions of voltage, angle, and frequency. The lack of assumptions on the form of that functions gives GridDyn enormous flexibility in defining and adding models

## Slide 19: Link Object
r<<x
G<<B and most of the time 0, for shorter lines B is also often 0
P1
Q1
g and b are the calculated admittances from r and x
Bus 1
Bus 2
r
x
G/2
G/2
jB/2
jB/2

## Slide 20: GridRelay
Source Object
Sink Object
Condition 1
Condition 2
Condition N
Action 1
Action 2
Action N
.
.
.
.
.
.
Delays
Condition to Action Matrix
Read data from Source objects(s) check conditions(continuously or at sampled intervals)
If condition(s) are met for a certain period of time trigger actions on sink object(s)

## Slide 21: GridRelay
Sensors build on the relay class and include a chain of control blocks for modeling sensing systems
Includes a communicator for interrelay interaction or communication with external controls or monitoring systems
Actions can be triggered off of 1 or more conditions
Implemented relays include
  Fuses
  Breakers
  Impedance based zonal relays
  Differential relays
  Load relays (voltage and frequency)
  Gen relays (voltage and frequency)
  Thermal models for transformers
  Lifespan modules for transformer
  Bus relay

## Slide 22: GridRelay
Further expansion will allows nearly arbitrary models to be executed inside GridDyn allowing generic FMU’s , generic state space models, and flexible interfaces to other simulators and model types
  This is in development

## Slide 23: GridArea
Container for other primary objects
Wide area control schemes such as AGC (work in progress)
Output functions for computing results across the entire area
Object management functions

## Slide 24: GridLoad
basic load Implements a ZIP load model
  constant impedance(Z) (Yp, Yq)
  Constant Current(I) (Ip, Iq)
  Constant Power (P) (P, Q)
Total is the sum of all components power
P and Q are only functions of V for most loads
Also available are functional loads (ramp, sin, pulse, random)
And some other functions, or file input
And motor loads
And loads that interact with GridLab-D

## Slide 25: GridDynGenerator
GridDynGenerator
GenModel
P,Q
r
x
V
A
f
Governor
Pset
Exciter
PSS
Vtarget
w
P mech
Eq
Vs

## Slide 26: GridDynGenerator
All components are submodels
  Not all need to be present, Generators work with any or all types of components
  None of the components needs to know the internals of the other components, these submodels are the primary source of differential equations in power system models
Pset can be manipulated by AGC, and generator schedules
Vtarget can be manipulated by Wide area voltage controllers

## Slide 27: Other objects
Blocks --submodels which implement control system block
  Working on control system submodel which could implment arbritrary arrangements of blocks
  Gain, delay, deadband, function, pid, control, transferfunction, derivative, integral, and others available
Sources –basically signal generators into GridDyn
Schedulers– objects which control the scheduled power of things in Griddyn (generators, ties, loads)
  Manage generator ramps
  Coordinate AGC, reserve, and normal scheduled power
  Communicate via communicators