## Slide 1: Validation and Performance in Griddyn
GridDyn Documents
Philip Top

## Slide 2: Outline
Matpower test cases
Performance improvements
Scalable Test Cases
Profiling
Opportunities for parallelism

## Slide 3: Matpower test cases
Matpower is an open source power flow solver written in Matlab
  The solution engine itself is a newton raphson solver using KLU under the hood and can run in parallel.
28 test cases supplied with the Matpower source code
All in an *.m file format that can be read by MatPower
Griddyn can read those same source files to generate a solution which can be directly compared.

## Slide 4: Matpower test cases
Range in size from 4 busses to 9241 busses
These test cases were used as a validation/performance test for Griddyn.
Tested with identical results to tolerance levels.

## Slide 5: Execution Time comparison

## Slide 6: Matpower vs Release version

## Slide 7: Performance comparison

## Slide 8: Performance Improvements
Notes: V1 through v6 should be reversed V6 shows the most speedup.

## Slide 9: Performance Improvements
V1 Baseline –First trial
V2 15%(22%) improvement- change some function calls to reduce dynamic memory allocation
V3 50%(63%) improvement – add dedicated arrayData class for Kinsol sparse matrix object –so data is directly loading into the matrix –doesn’t work for first jacobian call since matrix is not filled out yet
V4 15%(24%) attempt 1 at speeding up matrix sorting. A Large chunk of time dedicated to sort operation to fill up sparse matrix at first call
V5 4 %(4.5%) move to boost small Vector class(1%), change KINSOL KLU to use AMD ordering instead of COLAMD (3%)
V6 7%(17%) Attempt 2 at speeding up arrayData operations for initial loading
Note X% (Y%) X is overall Y is for large test cases(>1000 busses)

## Slide 10: ArrayData class
Class used in jacobian related functions to store the sparse jacobian array
Main methods used in griddyn are
  assign(row,col, val);
  assignCheck(row,col,val) has additional logic to check the row and column to make sure they are valid and not add them if they are not
Designed for building a jacobian out of individual components in random order
  Elements are summed not replaced
  So structure must be cleared before start of operation
In the structure used in Griddyn the row and col are not necessarily unique
  So they are sorted and compacted before reading and loading into the sundials specific structure
  Previous version used a tuple for storing in a vector
  Assign operation very fast
  Sort was the slow part

## Slide 11: Efforts to speed up arrayData operations
Different sort algorithms (all worse)
Tried using the boost array classes from ublas (all slower, some substantially)
Wrapping the Sundials sparse matrices in a ArrayData object sped it up for all but the first call- in which case the column locations were not yet defined
  Fill by going to column and doing a brute force search of the rowindex for the right row
    Tried a find algorithm to do it but the overhead of that required at least 7 elements to be faster and very few columns have 7 elements or more so that ended up being slower than a simple internal loop

## Slide 12: Array Data current implementation
Go back to using a std::vector pairs, except packing the row and column in a single 32 bit number via bitshifting
So the sort is just on the first element of a pair instead of a tuple
  If we have more than 65535 states use a 64 bit number for the packing
Then split the storage into 2M bins
  Sort operation is N*logN with 2M bins this becomes N*log(N/2M) at the expense of at least 2x memory and additional operations on read and write.
  I am still tinkering with it a little
target goal is another 20% speedup in solution time for 2k to 40k busses for serial implementation
  -but the time spent is distributed throughout many different parts of the system and many function call so there is no obvious place to speed up any more.

## Slide 13: Testing for scalability
Wanted to get to very large test cases
  Design a set of scalable test cases that can test a wide range of bus counts
Really push the system and see where time is being spent
Use some of the unique capabilities in the XML readers
  Namely variable defines and Arrays so we can programmatically override definitions in the XML file and change the construction.

## Slide 14: Scalable test case
.
.
.

## Slide 15: Scalable test Case
Form a lattice of busses
A generator for every 9 busses
  Power output is scaled to accommodate loading and the network losses
A constant load on every bus
A motor load for every 4 busses
Generator near the middle is the slack bus

## Slide 16: Scalable test case
Size specified in an XML file garraySize variable
  Not all sizes produce a convergent case but most do.
  garraySize specifies the number of busses along an edge
  For a total of garraySize^2 busses
4 different files
  Swing in corner
  Swing in Center ( 4 lines per bus) (can go the biggest so far)
  Swing in Center with single diagonal (6 lines per bus)
  Swing in Center with full diagonal (8 lines per bus)
More scalable test cases are in development

## Slide 17: Scalable test cases
Between the 4 of them can test algorithm scaling,
relative scaling of different components
Performance scaling and testing
Isolation of the effect of decreasing sparsity with constant state count
These are flat start, hard cases with non-linearities in the network and in the load.

## Slide 18: Scalable test case block_grid3
.
.
.

## Slide 19: Scalable test case block_grid4
.
.
.

## Slide 20: Voltage Results

## Slide 21: Angle Results

## Slide 22: Angle Results

## Slide 23: Results
Tests on 9 to 446224 busses -> 20 to 1004004 states
Busses | Solve Time (s)
100 | 0.0057
400 | 0.016
1024 | 0.0449
2500 | 0.138
10000 | 0.864
26896 | 3.679
101124 | 144.38
446224 | 405.14
Notes: Time is wall time elapsed from call to solve function to return

## Slide 24: Time to Solution Breakdown
Notes: A couple things really stand out.
1). The time spent in loading the simulation from XML is more than the single power flow time until around 50K busses ( I haven’t spent much time speeding this up)
2). The time in KINSOL is where the time growth using higher and higher percentages of the total simulation time.

## Slide 25: Order of various parts
N is number of non-zeros element in jacobian
Load is ~ 1.85x10-5*N (continuously being improved)
Init is O(N) ~10-6*N
Resid is O(NlogN) N from the resid function itself and ~logN number of iterations
Jacobian is O(NlogN) about 2x more time than residual
  Looking at solvers that reduce number of jacobian calls
Kinsol seems to be something like O(N1.6) but multiplier is really small

## Slide 26: Time in the solve Function
Notes: Red/Green are in Griddyn code
Blue in Sundials code

## Slide 27: Where we are spending time

## Slide 28: Bottom Up Time
Klu_refactor (25%)
Klu_kernel (3.0%)
New (2.3%)
String ops (~, compare, begin, to_string) 7.4%
  All in loading

## Slide 29: Other Tidbits

## Slide 30: Other Tidbits
5 NR iterations to 12000 busses
6 NR iterations to 27000 busses
7 NR iterations to 44000 busses
8 NR iterations up ~160000 busses
160000 busses took 2.6GB of memory
1000000 busses took ~18 GB of memory

## Slide 31: Opportunities for Parallelism
Up to 13000 busses a majority of time is spend in Griddyn Code
Residual function could be parallelized
  state data is constant –no changes
  All changes happen in resid array and only on individual objects own specific locations—no memory conflicts so object calculations could be parallelized
Jacobian is more interesting since it is a bigger chunk of time
  Some collision avoidance may be necessary in the arrayData structure
  Each Jacobian row is written to only by a single object
  A compressed row matrix sparse matrix might be more amenable to parallelization efforts– scheduled to be added for next release of sundials (Aug/Sep 2016, gridDyn will be updated at that time)